## Slide 1
CertGCS at a glance — why planner outputs must be validated, and why validation is cheap
① Birth of the probabilistic map (offline)
IrisZo convex decomposition
point oracle + hyperplane cuts + Bernoulli (ε,δ) gate
non-convex C-obstacles ⇒ every cut is only local
Region map: 97% of the volume truly free
+ 3.2% residual pockets — ε>0 by construction
pockets live on boundary shells / door jambs
② The amplification law — the optimizer is a search engine for model errors, not a sampler
3.2% volume error
uniform measure: darts into the regions
12.5% random-query answers invalid
2/16 benchmark optima, two machines
62% task-query answers invalid
18/29, deepest −91 mm
×4
×5
① Taut paths patrol the boundary
a shortest path hugs walls and cuts corners — exactly where the pockets live
② The argmin harvests model surplus
if the through-pocket shortcut is shorter, EVERY modeled optimum takes it; the exacter the solver, the surer
③ Tasks live in the dirty real estate
grasp poses hug the shelves = where the generator truncated deepest; task corridors follow them
Measure mismatch: audits sample the uniform measure, the planner samples the argmin measure — the only aligned test is a test of the argmin itself (↓ our layer)
③ The certified layer (online) — the necessary thing, done the cheap way
Region map
from ① — 97% clean = why checking is cheap
Interface sampling + informed pruning
admissible LB keys; pruned- subgraph LB stays valid
Search → candidate
anytime incumbent; monotone improvement
Validate ONLY the candidate
lineage 2, lazy: never the graph — just the answer
Certificate-ball chain covers the whole path
lineage 1: one distance query frees a whole ball
SOCP polish → re-validate
convex optimum in corridor; polish is an argmin too
Certified path + ε-cert or honest no-path
LB ≤ c* ≤ certified UB; degrades gracefully
dirty segment → in-region repair (convexity keeps via points legal) → unfixable: blacklist the edge
the lazy loop: delete → re-search → re-validate, until certified or honestly infeasible
Lineage 2 · lazy collision checking — LazyPRM (Bohlin & Kavraki '00) / LazySP (Dellin & Srinivasa '16)
“Navigate first, repair later — only the roads the route uses.”
Most edges are never used by any shortest path → assume all valid, search, then check only the returned path's edges; delete failures, re-search.
Our twist: the skeleton is the IRIS adjacency graph (no PRM to build), and what gets validated is the argmin of convex optimization — the antidote to the amplification law.
Lineage 1 · safety certificates — Bialkowski/Karaman/Frazzoli (WAFR'12/IJRR'16) → Safe Bubble Cover (ISRR'24)
“One distance query, one ball exempt”: clearance φ(q) ⇒ the ball of radius φ(q)/L is provably safe (L = robot Lipschitz constant).
Overlapping balls chained along the segment = a continuous proof: no resolution parameter, no loophole; long strides in the open, fine steps near obstacles.
Measured: ~200 calls × 2.3 ms per path, certificates in 0.02–0.06 s — cheap because the map is 97% clean (the dividend of ①).
E16 head-to-head (29 task queries, same library & machine): reference delivers 21/29 invalid (18 probe-confirmed) vs ours 0 invalid (15 certified + 14 honest no-paths) · first certified answer 1.14 s < 1.59 s for the unvalidated one · cost ratio 1.0000 on clean pairs · price of truth only where the reference is wrong: median +14%
All three routes to a stricter library fail (strict gate: 47 regions, 0 portals / C-IRIS: 7 islands / margins: contamination flat, connectivity lost first) — volume-level certainty is unaffordable; the path-level certificate does the necessary thing, the cheap way.